KoggerSonic
kogger.tech

Serial Binary Protocol (SBP) specification

Document Information
Number	KS_SBP_100
Date	12.10.19
Revision	1.0.0
Status	Early Production Information

# Introduction
## Protocol frame structure
Header		Range over which the checksum is calculated				Checksum
SYNC1	SYNC2	LENGTH	MODE	ID	PAYLOAD	CHECK1	CHECK2
U1	U1	U1	U1	U1	BYTE[LENGTH]	U1	U1
0xBB	0x55	0 … 128	0 … 255	1 … 255	—	0 … 255	0 … 255

MODE
Name	Bits	Description
TYPE	0:2 bit	Field defines the type and purpose of the data
VERSION	3:5 bit	Field defines the data version
MARK	6 bit	Set by the host and reset when the device reboots. Used only for direction of device-host
RESPONSE	7 bit	Request response to the command. Used only for direction of host-device

TYPE of MODE
TYPE	Value	Description
RSERVED	0	Reserved
CONFIRM	1	Confirmation
SETTING	2	Setting parameters
GETTING	3	Request data
CONTENT	4	Content of data
ACTION	5	Action request
REACTION	6	Reaction on action request
RSERVED	7	Reserved

## Checksum
The checksum algorithm used is the Fletcher-16.
Example source code for calculating the checksum:
uint8_t CHECK1 = 0;
uint8_t CHECK2 = 0;

void CheckSumUpdate(uint8_t byte) {
CHECK1 += byte;
CHECK2 += CHECK1;
}
## Number Formats
All multi-byte values are ordered in Little Endian format.
All floating point values are transmitted in IEEE754 single or double precision.
All bit-field in LSB format.
Name	Type	Size (Bytes)	Range
S1	int8_t	1	-128 ... 127
U1	uint8_t	1	0 … 255
S2	int16_t	2	-32768 … 32767
U2	uint16_t	2	0 … 65535
S4	int32_t	4	-2'147'483'648 ... 2'147'483'647
U4	uint32_t	4	0 … 4'294'967'295
F4	float	4	-1*2^+127 ... 2^+127
D8	double	8	-1*2^+1023 ... 2^+1023

# Command specification
## Command overview
Name	ID	Description
CMD_RESP	0x01	Command response
CMD_CHART	0x0A	Working with data in chart format
CMD_YPR	0x0C	Attitude in Euler angels
CMD_QUAT	0x0D	Attitude in Quaternion
CMD_TEMP	0x12	Temperature data
CMD_DIAG*	0x13	Diagnostic data
CMD_TRANSC	0x15	Transceiver settings
CMD_SND_SPEED	0x16	Sound speed settings
CMD_UART	0x17	UART settings
CMD_CLB_GYR*	0x18	Calibrate gyroscope
CMD_CLB_ACC*	0x19	Calibrate accelerometer
CMD_FLASH	0x1D	Flash in-run settings to the built-in non-volatile memory
CMD_RESTORE	0x1E	Restore default settings and reboot
CMD_REBOOT	0x1F	Reboot device
CMD_MARK	0x20	Setting the mark of continuous work (non-reboot) device
CMD_VERSION*	0x21	Software and hardware version information
CMD_LOAD_UPD*	0x23
CMD_FW_RUN*	0x24
CMD_BOOT_RUN*	0x25

* In developing
## CMD_RESP (ID 0x01)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [6]
		Type	Range	Default	Unit	Description
CODE		U1
LENGTH		U1
MODE		U1
ID		U1
CHECK1		U1
CHECK2		U1

## CMD_CHART (ID 0x0A)
Message format
Mode	Version	Direction		Description
ACTION	0	Host to Device		Get chart with update settings
CONTENT	0	Device to Host		Content settings of Chart
Payload format [14]
		Type	Range	Default	Unit	Description
STRT_POS		U4	0 …		mm
ITEM_COUNT		U2	1 ... 5000		—
ITEM_RESOL		U2	10 ... 1000		mm	Item resolution
REPEAT_PERIOD		U2	0 ... 65535		ms	0 — for single response / >0 — for periodic response
RESERVED		U4	0	0	—

Message format
Mode	Version	Direction		Description
REACTION	0	Device to Host		Data of chart
Payload format [8+1*N]
		Type	Range	Default	Unit	Description
STRT_POS		U4			mm
ITEM_OFFSET		U2			—
ITEM_RESOL		U2			mm
CHART		U1[N]		—		Data of chart. The maximum data length in one packet is 100.

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device		Get setting of Chart
ACTION	0	Host to Device		Get chart without update settings
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_YPR (ID 0x0C)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host		Attitude information in Euler 321 format
Payload format [6]
		Type	Range	Default	Unit	Description
YAW		S2	-18000 ...18000		0.01 deg	Yaw
PITCH		S2	-18000 ...18000		0.01 deg	Pitch
ROLL		S2	-18000 ...18000		0.01 deg	Roll

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device		Request attitude information in Euler 321 format
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
Mode	Version	Direction		Description
SETTING	1	Host to Device
CONTENT	1	Device to Host
GETTING	1	Host to Device
Payload format [2]
		Type	Range	Default	Unit	Description
ATTACH		U1		0		0 — no attach, / 1 — attach

## CMD_QUAT (ID 0x0D)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host		Attitude information in quaternion format
Payload format [16]
		Type	Range	Default	Unit	Description
W0		float			—
W1		float			—
W2		float			—
W3		float			—

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device		Request attitude information in quaternion format
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_TEMP (ID 0x12)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [8]
		Type	Range	Default	Unit	Description
TEMP_IMU		S2			0.01 °C
TEMP_CPU		S2			0.01 °C

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device		Request temperature
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_DIAG (ID 0x13) (In developing)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [34]
		Type	Range	Default	Unit	Description
UPTIME		U4			ms
TEMP_IMU		S2			0.01 °C
TEMP_CPU		S2			0.01 °C
TEMP_MIN		S2			0.01 °C
TEMP_MAX		S2			0.01 °C
SYS_VOLT		U2			mV
BOOST_VOLT		U2			mV
DET_VOLT		U2			mV
DET_NOISE		U2			mV
AGC_GATE_VOLT		U2			mV
RESERVED		U4
RESERVED		U4
RESERVED		U4

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_TRANSC (ID 0x15)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
SETTING	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
FREQ		U2		675	kHz	Frequency
PULSE		U1		10	COUNT
BOOST		U1		1	—
RESERVED		U4		0	—

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_SND_SPD (ID 0x16)
Sound speed
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
SETTING	0	Host to Device
Payload format [6]
		Type	Range	Default	Unit	Description
SOUND_SPEED		U2		1500	m/s	Sound speed
RESERVED		U4		0	—

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_UART (ID 0x17)
Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
SETTING	0	Host to Device
Payload format [13]
		Type	Range	Default	Unit	Description
UART_KEY		U4	—	0xC96B 5D4A	—
UART_ID		U1	1 ...	1	—
BAUDRATE		U4	9600 … 921600	115200	bps
RESERVED		U4	0	0

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device
Payload format [5]
		Type	Range	Default	Unit	Description
UART_KEY		U4		0xC96B 5D4A	—
UART_ID		U1	1 ...	1	—

## CMD_CLB_GYR (ID 0x18) (In developing)
Message format
Mode	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_CLB_ACC(ID 0x19) (In developing)
Message format
Mode	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_FLASH (ID 0x1D)
Flash settings to non-volatile memory
Message format
Mode	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_RESTORE (ID 0x1E)
Restore default settings
Message format
Mode	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_REBOOT (ID 0x1F)
Message format
Mode	Version	Direction		Description
ACTION	0	Host to Device
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_MARK (ID 0x20)
Message format
Mode	Version	Direction		Description
SETTING	0	Host to Device
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [1]
		Type	Range	Default	Unit	Description
MARK		U1			—

## CMD_VERSION (ID 0x21) (In developing)
Message format
Mode	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
Mode	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [21]
		Type	Range	Default	Unit	Description
SW_BOOT_VER		U4		—	—
SW_FW_VER		U4		—	—
HW_VER		U4		—	—
HW_FTRS		U4		—	—
SERIAL_NBR		U4		—	—
PART_NBR		U1[12]		—	—
FACTORY_DATE		U2		—	—