KoggerSonic
kogger.tech

Serial Binary Protocol (SBP) specification

Document Information
Number	KS_SBP_100
Date	11.11.19
Revision	1.0.0
Status	Early Production Information

# Introduction
## Protocol frame structure
Header		Range over which the checksum is calculated				Checksum
SYNC1	SYNC2	LENGTH	MODE	ID	PAYLOAD	CHECK1	CHECK2
U1	U1	U1	U1	U1	BYTE[LENGTH]	U1	U1
0xBB	0x55	0 … 128	0 … 255	1 … 255	—	0 … 255	0 … 255

MODE
Name	Bits	Description
TYPE	0:2 bit	Field defines the type and purpose of the data
VERSION	3:5 bit	Field defines the data version
MARK	6 bit	Once device is switched on, this flag is always in reset state (ZERO). It can be set to active state (ONE) by the host (see the CMD_MARK command) and the slave device keeps the flag in active state in every frame until hardware reset occurs or is reset by the host. Therefore the host monitors the device's actual settings.
RESPONSE	7 bit	HOST → DEVICE: / Set the flag to active state (ONE) in order to get the result of processing the command. The flag doesn't affect the response if one is provided by the TYPE field. / DEVICE → HOST: / The flag is in reset state (ZERO) by default. Payload goes according to the command specification. If flag is set, the payload contains the result of command processing (see CMD_RESP command).

TYPE of MODE
TYPE	Value	Description
RSERVED	0	Reserved
CONFIRM	1	Confirmation
SETTING	2	Setting parameters
GETTING	3	Request data
CONTENT	4	Content of data
ACTION	5	Action request
REACTION	6	Reaction on action request
RSERVED	7	Reserved

## Checksum
The checksum algorithm used is the Fletcher-16.
Example source code for calculating the checksum:
uint8_t CHECK1 = 0;
uint8_t CHECK2 = 0;

void CheckSumUpdate(uint8_t byte) {
CHECK1 += byte;
CHECK2 += CHECK1;
}
## Number Formats
All multi-byte values are ordered in Little Endian format.
All floating point values are transmitted in IEEE754 single or double precision.
All bit-field in LSB format.
Name	Type	Size (Bytes)	Range
S1	int8_t	1	-128 ... 127
U1	uint8_t	1	0 … 255
S2	int16_t	2	-32768 … 32767
U2	uint16_t	2	0 … 65535
S4	int32_t	4	-2'147'483'648 ... 2'147'483'647
U4	uint32_t	4	0 … 4'294'967'295
F4	float	4	-1*2^+127 ... 2^+127
D8	double	8	-1*2^+1023 ... 2^+1023

# Command specification
## Command overview
Name	ID	Description
CMD_TIMESTAMP	0x02
CMD_CHART	0x0A	Working with data in chart format
CMD_YPR	0x0C	Attitude in Euler angles
CMD_QUAT	0x0D	Attitude in Quaternion
CMD_TEMP	0x12	Temperature data
CMD_DIAG*	0x13	Diagnostic data
CMD_TRANSC	0x15	Transceiver settings
CMD_SND_SPEED	0x16	Sound speed settings
CMD_UART	0x17	UART settings
CMD_CLB_GYR*	0x18	Calibrate gyroscope
CMD_CLB_ACC*	0x19	Calibrate accelerometer
CMD_FLASH	0x1D	Flash in-run settings to the built-in non-volatile memory
CMD_RESTORE	0x1E	Restore default settings and reboot
CMD_REBOOT	0x1F	Reboot device
CMD_MARK	0x20	Setting the mark of continuous work (non-reboot) device
CMD_VERSION*	0x21	Software and hardware version information
CMD_LOAD_UPD*	0x23
CMD_FW_RUN*	0x24
CMD_BOOT_RUN*	0x25

* In developing
## CMD_RESP (In developing)
Contains the result of command processing. Can be used as a check if the command is processed correctly. The MODE and ID fields are the same as in the initiating command.
Message format
TYPE	Version	Direction		Description
...	...	Device to Host
Payload format [6]
		Type	Range	Default	Unit	Description
CODE		U1				The field contains the response code of processing the command.
CHECK1		U1				Command checksum
CHECK2		U1

## CMD_TIMESTAMP(ID 0x02)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host		Timestamp from Device
CONTENT	1	Local		Timestamp from Logging
Payload format [4]
		Type	Range	Default	Unit	Description
TIMESTAMP		U4	0 …		ms	Timestamp

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device		Request Timestamp
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_CHART (ID 0x0A)
Message format
TYPE	Version	Direction		Description
ACTION	0	Host to Device		Get chart with update settings
CONTENT	0	Device to Host		Content settings of Chart
Payload format [14]
		Type	Range	Default	Unit	Description
STRT_POS		U4	0 …		mm
ITEM_COUNT		U2	1 ... 5000		—
ITEM_RESOL		U2	10 ... 1000		mm	Item resolution
REPEAT_PERIOD		U2	0 ... 65535		ms	0 — for single response / >0 — for periodic response
RESERVED		U4	0	0	—

Message format
TYPE	Version	Direction		Description
REACTION	0	Device to Host		Data of chart
Payload format [8+1*N]
		Type	Range	Default	Unit	Description
STRT_POS		U4			mm
ITEM_OFFSET		U2			—
ITEM_RESOL		U2			mm
CHART		U1[N]		—		Data of chart. The maximum data length in one packet is 100.

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device		Get setting of Chart
ACTION	0	Host to Device		Get chart without update settings
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_YPR (ID 0x0C)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host		Attitude information in Euler 321 format
Payload format [6]
		Type	Range	Default	Unit	Description
YAW		S2	-18000 ...18000		0.01 deg	Yaw
PITCH		S2	-18000 ...18000		0.01 deg	Pitch
ROLL		S2	-18000 ...18000		0.01 deg	Roll

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device		Request attitude information in Euler 321 format
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_QUAT (ID 0x0D)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host		Attitude information in quaternion format
Payload format [16]
		Type	Range	Default	Unit	Description
W0		float			—
W1		float			—
W2		float			—
W3		float			—

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device		Request attitude information in quaternion format
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_TEMP (ID 0x12)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [8]
		Type	Range	Default	Unit	Description
TEMP_IMU		S2			0.01 °C
TEMP_CPU		S2			0.01 °C

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device		Request temperature
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_DIAG (ID 0x13) (In developing)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [34]
		Type	Range	Default	Unit	Description
UPTIME		U4			ms
TEMP_IMU		S2			0.01 °C
TEMP_CPU		S2			0.01 °C
TEMP_MIN		S2			0.01 °C
TEMP_MAX		S2			0.01 °C
SYS_VOLT		U2			mV
BOOST_VOLT		U2			mV
DET_VOLT		U2			mV
DET_NOISE		U2			mV
AGC_GATE_VOLT		U2			mV
RESERVED		U4
RESERVED		U4
RESERVED		U4

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_TRANSC (ID 0x15)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
SETTING	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
FREQ		U2		675	kHz	Frequency
PULSE		U1		10	COUNT
BOOST		U1		1	—
RESERVED		U4		0	—

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_SND_SPD (ID 0x16)
Sound speed
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
SETTING	0	Host to Device
Payload format [6]
		Type	Range	Default	Unit	Description
SOUND_SPEED		U2		1500	m/s	Sound speed
RESERVED		U4		0	—

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## CMD_UART (ID 0x17)
Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
SETTING	0	Host to Device
Payload format [13]
		Type	Range	Default	Unit	Description
UART_KEY		U4	—	0xC96B 5D4A	—
UART_ID		U1	1 ...	1	—
BAUDRATE		U4	9600 … 921600	115200	bps
RESERVED		U4	0	0

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device
Payload format [5]
		Type	Range	Default	Unit	Description
UART_KEY		U4		0xC96B 5D4A	—
UART_ID		U1	1 ...	1	—

## CMD_CLB_GYR (ID 0x18) (In developing)
Message format
TYPE	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_CLB_ACC(ID 0x19) (In developing)
Message format
TYPE	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_FLASH (ID 0x1D)
Flash settings to non-volatile memory
Message format
TYPE	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_RESTORE (ID 0x1E)
Restore default settings
Message format
TYPE	Version	Direction		Description
ACTION	0	Host to Device
Payload format [8]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_REBOOT (ID 0x1F)
Message format
TYPE	Version	Direction		Description
ACTION	0	Host to Device
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## CMD_MARK (ID 0x20)
Message format
TYPE	Version	Direction		Description
SETTING	0	Host to Device
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [1]
		Type	Range	Default	Unit	Description
MARK		U1			—

## CMD_VERSION (ID 0x21) (In developing)
Message format
TYPE	Version	Direction		Description
GETTING	0	Host to Device
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
TYPE	Version	Direction		Description
CONTENT	0	Device to Host
Payload format [21]
		Type	Range	Default	Unit	Description
SW_BOOT_VER		U4		—	—
SW_FW_VER		U4		—	—
HW_VER		U4		—	—
HW_FTRS		U4		—	—
SERIAL_NBR		U4		—	—
PART_NBR		U1[12]		—	—
FACTORY_DATE		U2		—	—