KoggerSonar
kogger.tech

Serial Binary Protocol (SBP) specification

Document Information
Number	KS_SBP_100
Date	Jan 8, 2020
Revision	2.0.0
Status	Early Production Information

# Introduction
## Protocol frame structure
Header		Range over which the checksum is calculated					Checksum
SYNC1	SYNC2	ROUTE	MODE	ID	LENGTH	PAYLOAD	CHECK1	CHECK2
U1	U1	U1	U1	U1	U1	BYTE[LENGTH]	U1	U1
0xBB	0x55	BITFIELD	BITFIELD	1 … 255	0 … 128	BYTEARRAY	0 … 255	0 … 255

ROUTE
Name	Bits	Description
DEV_ADDRESS	0:3 bit	Device address. Default address is 0x0. Broadcast address is 0xF.
RESRVED	3:7 bit	Reserved

MODE
Name	Bits	Description
TYPE	0:1 bit	Field defines the type and purpose of the data / 0 — Reserved, / 1 — CONTENT: DEVICE → HOST / 2 — SETTING: HOST → DEVICE / 3 —GETTING: HOST → DEVICE
RESERVED	2 bit	Reserved
VERSION	3:5 bit	Field defines the payload data version
MARK	6 bit	Once device is switched on, this flag is always in reset state (ZERO). It can be set to active state (ONE) by the host (see the ID_MARK) and the slave device keeps the flag in active state in every frame until hardware reset occurs or is reset by the host. Therefore the host monitors the device's actual settings.
RESPONSE	7 bit	HOST → DEVICE: / Set the flag to active state (ONE) in order to get the result of processing the command. The flag doesn't affect the response if one is provided by the TYPE field. / DEVICE → HOST: / The flag is in reset state (ZERO) by default. Payload goes according to the command specification. If flag is set, the payload contains the result of command processing (see RESP).

## Checksum
The checksum algorithm used is the Fletcher-16.
Example source code for calculating the checksum:
uint8_t CHECK1 = 0;
uint8_t CHECK2 = 0;

void CheckSumUpdate(uint8_t byte) {
CHECK1 += byte;
CHECK2 += CHECK1;
}
## Number Formats
All multi-byte values are ordered in Little Endian format.
All floating point values are transmitted in IEEE754 single or double precision.
All bit-field in LSB format.
Name	Type	Size (Bytes)	Range
S1	int8_t	1	-128 ... 127
U1	uint8_t	1	0 … 255
S2	int16_t	2	-32768 … 32767
U2	uint16_t	2	0 … 65535
S4	int32_t	4	-2'147'483'648 ... 2'147'483'647
U4	uint32_t	4	0 … 4'294'967'295
F4	float	4	-1*2^+127 ... 2^+127
D8	double	8	-1*2^+1023 ... 2^+1023

# Command specification
## Command overview
Name	ID	Description
ID_TIMESTAMP	0x02
ID_DATASET	0x07	Dataset management for automatic output
ID_DIST_SETUP	0x08	Detection Settings to Get Distance
ID_DIST_DATA	0x09	Distance data
ID_CHART_SETUP	0x0A	Chart Settings
ID_CHART_DATA	0x0B	Chart data in reflection patterns
ID_YPR	0x0C	Attitude in Euler angles
ID_QUAT	0x0D	Attitude in Quaternion
ID_TEMP	0x12	Temperature data
ID_DIAG*	0x13	Diagnostic data
ID_TRANSC	0x15	Transceiver settings
ID_SND_SPEED	0x16	Sound speed settings
ID_UART	0x17	UART settings
ID_CLB_GYR*	0x18	Calibrate gyroscope
ID_CLB_ACC*	0x19	Calibrate accelerometer
ID_FLASH	0x1D	Flash in-run settings to the built-in non-volatile memory
ID_RESTORE	0x1E	Restore default settings and reboot
ID_REBOOT	0x1F	Reboot device
ID_MARK	0x20	Setting the mark of continuous work (non-reboot) device
ID_VERSION*	0x21	Software and hardware version information
ID_LOAD_UPD*	0x23	Load Firmware update
ID_FW_RUN*	0x24	Run Firmware
ID_BOOT_RUN*	0x25	Run Bootloader

* In developing
## RESP
Contains the result of command processing. Can be used as a check if the command is processed correctly. The MODE and ID fields are the same as in the initiating command.
Message format
TYPE	Version	Direction		Description
...	...	DEVICE → HOST
Payload format [6]
		Type	Range	Default	Unit	Description
CODE		U1				The field contains the response code of processing the command.
CHECK1		U1				Command checksum
CHECK2		U1

## ID_TIMESTAMP(ID 0x02)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST		Timestamp from Device
Payload format [4]
		Type	Range	Default	Unit	Description
TIMESTAMP		U4	0 …		ms	Timestamp

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Request Timestamp
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_DATASET (0x07)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
CONTENT	0	DEVICE → HOST
Payload format [8]
		Type	Range	Default	Unit	Description
PERIOD_1		U2	0 ... 65535	0	ms	0 — for disable periodic response / >0 — for periodic response with period by value [ms]
MASK_1		U2	BITFIELD	0x00
PERIOD_2		U2	0 ... 65535	0	ms	0 — for disable periodic response / >0 — for periodic response with period by value [ms]
MASK_2		U2	BITFIELD	0x00

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Get data of CHART
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_DIST_SETUP (0x08)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST		Data of chart
Payload format [9]
		Type	Range	Default	Unit	Description
MAX_NUMBER		U1	1 … 10	1
ABS_OFFSET		U4	0 ...	0	mm
RANGE		U4	0 ...	50000	mm

## ID_DIST_DATA (0x09)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST		Data of chart
Payload format [8]
		Type	Range	Default	Unit	Description
NUMBER		U1
STRONG		U1
RANGE		U4	0 ...		mm
WIDTH		U2	0 ...		mm

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Get Range
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_CHART_SETUP (0x0A)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
CONTENT	0	DEVICE → HOST
Payload format [6]
		Type	Range	Default	Unit	Description
SAMPLE_COUNT		U2	1 ... 5000		—	Sample count
SAMPLE_RESOL		U2	10 ... 1000		mm	Sample resolution
ABS_OFFSET		U2	0 …			Absolute Offset in number of sample

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Get setting of Chart
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_CHART_DATA (0x0B)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST		Data of chart
Payload format [6+1*N]
		Type	Range	Default	Unit	Description
SEQ_OFFSET		U2	0 …			Sample Offset in Sequence
SAMPEL_RESOL		U2	10 …		mm	Samples resolution
ABS_OFFSET		U2	0 ...			Absolute Offset in sample number for Sequence
CHART		U1[N]	ARRAY			Data of chart. The maximum data length in one packet is 100.

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Get data of CHART
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_YPR (0x0C)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST		Attitude information in Euler 321 format
Payload format [6]
		Type	Range	Default	Unit	Description
YAW		S2	-18000 ...18000		0.01 deg	Yaw
PITCH		S2	-18000 ...18000		0.01 deg	Pitch
ROLL		S2	-18000 ...18000		0.01 deg	Roll

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Request attitude information in Euler 321 format
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_QUAT (0x0D)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST		Attitude information in quaternion format
Payload format [16]
		Type	Range	Default	Unit	Description
W0		float			—
W1		float			—
W2		float			—
W3		float			—

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Request attitude information in quaternion format
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_TEMP (0x12)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
Payload format [4]
		Type	Range	Default	Unit	Description
TEMP_IMU		S2			0.01 °C
TEMP_CPU		S2			0.01 °C

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE		Request temperature
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_DIAG (0x13) (In developing)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
Payload format [34]
		Type	Range	Default	Unit	Description
UPTIME		U4			ms
TEMP_IMU		S2			0.01 °C
TEMP_CPU		S2			0.01 °C
TEMP_MIN		S2			0.01 °C
TEMP_MAX		S2			0.01 °C
SYS_VOLT		U2			mV
BOOST_VOLT		U2			mV
DET_VOLT		U2			mV
DET_NOISE		U2			mV
AGC_GATE_VOLT		U2			mV
RESERVED		U4
RESERVED		U4
RESERVED		U4

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_TRANSC (0x15)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
FREQ		U2		675	kHz	Frequency
PULSE		U1		10	COUNT
BOOST		U1		1	—

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_SND_SPD (0x16)
Sound speed
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
SETTING	0	HOST → DEVICE
Payload format [2]
		Type	Range	Default	Unit	Description
SOUND_SPEED		U2		1500	m/s	Sound speed

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE
Payload format [0]
		Type	Range	Default	Unit	Description
No data

## ID_UART (0x17)
Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
SETTING	0	HOST → DEVICE
Payload format [9]
		Type	Range	Default	Unit	Description
UART_KEY		U4	—	0xC96B 5D4A	—
UART_ID		U1	1 ...	1	—
BAUDRATE		U4	9600 … 921600	115200	bps

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE
Payload format [5]
		Type	Range	Default	Unit	Description
UART_KEY		U4		0xC96B 5D4A	—
UART_ID		U1	1 ...	1	—

## ID_CLB_GYR (0x18) (In developing)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## ID_CLB_ACC(0x19) (In developing)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## ID_FLASH (0x1D)
Flash settings to non-volatile memory
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## ID_RESTORE (0x1E)
Restore default settings
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## ID_REBOOT (0x1F)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

## ID_MARK (0x20)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—

Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
Payload format [1]
		Type	Range	Default	Unit	Description
MARK		U1			—

## ID_VERSION (0x21) (In developing)
Message format
TYPE	Version	Direction		Description
GETTING	0	HOST → DEVICE
Payload format [0]
		Type	Range	Default	Unit	Description
No data

Message format
TYPE	Version	Direction		Description
CONTENT	0	DEVICE → HOST
Payload format [21]
		Type	Range	Default	Unit	Description
SW_BOOT_VER		U4		—	—
SW_FW_VER		U4		—	—
HW_VER		U4		—	—
HW_FTRS		U4		—	—
SERIAL_NBR		U4		—	—
PART_NBR		U1[12]		—	—
FACTORY_DATE		U2		—	—

## ID_BOOT_RUN (0x1F)
Message format
TYPE	Version	Direction		Description
SETTING	0	HOST → DEVICE
Payload format [4]
		Type	Range	Default	Unit	Description
KEY		U4		0xC96B 5D4A	—